## Slide 1: Memo on Optical Connections
A. Pellegrino
Nikhef, 3-Sep-2020
To/From Host
TTC

## Slide 2: Useful Links
Nikhef Redmine https://redmine.nikhef.nl/et/projects/atlas-felix/wiki/Atlas_setup_in_H148
  Kept up to date by Frans
Jos’public page https://www.nikhef.nl/~i73/Testlab.html
  Kept up to date by Jos

## Slide 3: Optical Breakout Panels MPOLC
1.
2.
3.

## Slide 4: MPOLC PP 1
MPO side: 48 Tx/Rx-crossed to TURANO Prime FLX-712
MTP to 6 LC Duplex
1-9
2-10
3-11
4-12
5,6,7,8 n.u.
Unplugged 40GB QSFP+ Fiber-Optics Transceiver
1-9
2-10
3-11
4-12
5,6,7,8 n.u.
Unplugged 40GB QSFP+ Fiber-Optics Transceiver
1-9
2-10
3-11
4-12
5,6,7,8 n.u.
Unplugged 40GB QSFP+ Fiber-Optics Transceiver
This is the only one actually used, by JJ’s VLDB

## Slide 5: MPOLC PP 2
Avago AFBR-83PDZ Fiber-Optic CXP Transceiver with 12 lanes in each direction for short-range multi-lane communication and interconnect (e.g. 100GbE and 1210G IB-QDR), each lane capable of operating at 10.3125 Gbps up to 100m (resp. 150m) using OM3 (resp. OM4) fiber (>120Gbps aggregate bandwidth) over multimode fiber systems using a nominal wavelength of 850 nm. The optical interface uses a 24-fiber MPO connector.
MPO side: 212duplex to ARGOS HGT-710
NO LC used anywhere

## Slide 6: MPOLC PP 3-1
MPO side: (48 Tx/Rx-crossed?) to AGOGNA (BNL-712?)
Simplex connection from MROD LC Data Tx
Henk’s VLDB
N.U.
used to test the simplex transmission CSMs  FELIX-MROD. In this case, the regular MROD is used as external data generator, emulating the data output from the CSM (Chamber Service Modules)

## Slide 7: Digression on MROD Connections
Simplex connection from MROD LC Data Tx
used to test the simplex transmission CSMs  FELIX-MROD. In this case, the regular MROD is used as external data generator, emulating the data output from the CSM (Chamber Service Modules)
Link 16 to AGOGNA (BNL-711 or BNL-712?)
MPO-to-4-LC-Duplex
MPO-to-4-LC-Duplex
MROD duplex channels (S-link protocol) connected to one of the two RobinNP in canche directly (no patch panel). Each RobinNP has 3 MPO-4-Duplex connectors.

## Slide 8: MPOLC PP 3-2
MPO side: (48 Tx/Rx-crossed?) to AGOGNA (BNL-712?)
All used as loop-back

## Slide 9: Overview
FELIX | FELIX Pair | MPOLC Cassette | Host
Turano FLX-712 | 24 | PP1 – Pair 24 | JJ VLDB

## Slide 10: Optical Fanout ST
From “Topo” Red Box
MROD TIM-3C
N.U.
N.U.
GIMONE (VC-709?)
TURANO (FXL-712)
AGOGNA (FXL-712)
1.6 db in
10.1 db out

## Slide 11: Optical Fanout ST
1. MROD TIM-3C
3. N.U.
10. GIMONE (VC-709?)
14. TURANO (FXL-712)
15. AGOGNA (FXL-712)
1.6 db in (from “Topo Red Box”)
10.1 db out
5. N.U.
4.7 db in (from TTC vi/ex)
12.2 db out
7.5 db
8.5 db

## Slide 12: Next
to buy extra fiber network components, I need to know:
  The exact optical connection configuration of each FPGA card (i.e. how many MPO8/12/24/48 they have)
  FLX Users and use cases. In my count, I see:
    Loop-back
    VLDB Henk
    VLDB JJ
    Forthcoming ITk-strips  VLDB+  FELIX (JJ)
    Forthcoming ITk-pixel  VLDB+  FELIX (JJ)
    FLX MROD
    FELIG  FELIX
    Bas’ mezzanine  FELIX
  TTC users and use cases
    With one or two cheap extra ST fanouts, we can have TTCvi, Topo and future-Zinc simultaneously in use